## Slide 1: AXI4-to-APB Bridge UVM Verification
UVM FINAL PROJECT
Dual-agent UVM environment, scoreboard, functional coverage and a 17-test regression for the PULP axi2apb RTL
AXI master agent
axi2apb DUT
APB slave agent
Muhammad Sheharyar
Submitted to Engr. Shahbaz Ahmad
Synopsys VCS · UVM 1.2
Notes: Introduce the project: a UVM environment to verify the PULP axi2apb bridge. The AXI master agent drives the bridge, the APB slave agent answers on the other side. Submitted to Engr. Shahbaz Ahmad.

## Slide 2: Project scope
Objective
Build a reusable UVM environment that verifies the supplied PULP axi2apb bridge.
Project rule
The DUT is never modified. Only testbench changes are allowed to make tests pass.
Spec deliverables covered
Dual-agent environment, AXI and APB agents, scoreboard, functional coverage, directed and random tests, regression.
Delivery
Milestone-based work in a GitHub repository, with the final verification report and a repeatable Makefile flow.
AXI2APB Bridge · UVM Verification
2
Notes: Source: the UVM final project specification. Key rule: the DUT must not be modified. The environment follows the spec milestones: dual-agent environment, agents, scoreboard and reference model, directed tests, random tests, regression and coverage.

## Slide 3: The DUT: axi2apb bridge
AXI4 slave port
AW · W · B · AR · R
5 buffers + FSM
fifo depth 4
APB master port
PENABLE · PADDR · PWDATA
Read has priority
In IDLE the FSM serves AR before AW.
Write needs AW and W
A write starts only when both are valid together.
Single-beat only
No burst support: AWLEN and ARLEN are buffered but ignored.
PSLVERR and WSTRB ignored
BRESP and RRESP are always OKAY. PSEL is tied to 1.
AXI2APB Bridge · UVM Verification
3
Notes: The DUT is the PULP axi2apb module with five channel buffers built on axi_single_slice and a generic fifo. These four RTL behaviours were documented and verified rather than assumed.

## Slide 4: Bridge FSM: five states
State | Behaviour | Next
IDLE | Read first; write needs AW and W | Any other state
WAIT_R_PREADY | PENABLE high, waits for PREADY | DONE_SINGLE_RD
WAIT_W_PREADY | PENABLE and PWRITE high, waits | SEND_B_RESP
DONE_SINGLE_RD | RVALID and RLAST until RREADY | IDLE
SEND_B_RESP | BVALID until BREADY | IDLE
PREADY is checked directly in IDLE, so a zero-wait APB slave moves IDLE straight to SEND_B_RESP or DONE_SINGLE_RD.
AXI2APB Bridge · UVM Verification
4
Notes: The FSM has five states. The last line matters later: it explains why the FSM coverage could not reach 100 percent.

## Slide 5: UVM environment architecture
AXI master agent
Sequencer · driver · monitor
axi2apb DUT
AXI in, APB out
APB slave agent
Sequencer · driver · monitor
AXI monitor, analysis port
APB monitor, analysis port
Scoreboard
Matches AXI and APB transactions
Coverage collector
Samples cg_axi and cg_apb
AXI2APB Bridge · UVM Verification
5
Notes: Both agents are active. The two monitors feed the scoreboard and the coverage collector through analysis ports, so every check is transaction based, not waveform based.

## Slide 6: The two agents
AXI master agent
Driver: VALID/READY handshakes on AW, W and AR, with BREADY and RREADY delays
Monitor: rebuilds complete read and write transactions from channel activity
Sequences: write, read, random and a single-item wrapper
APB slave agent
Driver: answers PREADY, PRDATA and PSLVERR with configurable wait states
Monitor: observes PSEL and PENABLE requests and their completion
Stimulus: programmable wait states, read data and error response
AXI2APB Bridge · UVM Verification
6
Notes: The AXI agent represents the AXI master side, the APB agent represents the APB slave side. Neither is RTL: both are testbench code.

## Slide 7: Scoreboard and coverage
Scoreboard
Keeps queues of AXI and APB transactions and matches them in order
Checks address, data, ID and USER propagation through the bridge
Checks that every AXI response is OKAY
Reports each mismatch as a UVM error
Functional coverage
Fed by both monitors through uvm_analysis_imp_decl
Two covergroups: cg_axi and cg_apb
Read vs write, APB wait states 0, 1 and 5
BREADY and RREADY delays, address and data patterns, plus crosses
AXI2APB Bridge · UVM Verification
7
Notes: The scoreboard compares transactions, not waveforms, as the spec asks. Coverage is collected from the same monitor streams.

## Slide 8: Repository structure
rtl/
DUT and channel buffers
tb/
Interfaces, UVM package, tb_top
uvm/
axi, apb and env components
sequences/
AXI stimulus sequences
tests/
Base test, 14 directed, 3 random
sim/
Makefile, build.flist, out/
scripts/
parse_log.py log parser
logs/
Simulation logs
results/
Regression summary
docs/
Verification plan and final report
The layout follows the folder structure required by the project specification.
AXI2APB Bridge · UVM Verification
8
Notes: Same methodology as the earlier APB project (docs, rtl, sim, tb) but extended to the full structure the spec asks for.

## Slide 9: 17 tests: 14 directed, 3 random
Directed
reset_test
axi_write_ready_test
axi_read_ready_test
axi_write_wait_test
axi_read_wait_test
bready_delay_test
rready_delay_test
rd_wr_priority_test
bk2bk_read_test
bk2bk_write_test
mixed_traffic_test
id_user_test
pslverr_test
coverage_closure_test
Constrained-random
rand_test
rand_axi_test (100 txns)
rand_mixed_test (100 txns)
Directed tests cover the spec list: reset, ready and wait states, BREADY and RREADY delay, read priority, back-to-back, mixed traffic, ID and USER, PSLVERR.
AXI2APB Bridge · UVM Verification
9
Notes: The highlighted coverage_closure_test was added to hit the remaining functional cross bins. Directed tests were written before the random ones, as the spec requires.

## Slide 10: Makefile: targets
Target | What it does
compile | VCS build of one test into out/build_TEST
sim | Compile, run with SEED, write the log, auto-parse it
gui | Open the waveform GUI
regression | Compile once, run all 17 tests, write regression_summary.txt
cov | Combined urg coverage report in out/coverage_report
clean, allclean | Remove one test build, or every build, log and result
Variables: TEST, SEED, VERBOSITY
make sim TEST=bk2bk_write_test SEED=5
AXI2APB Bridge · UVM Verification
10
Notes: Same build-folder methodology as the earlier APB project: one build folder per test, logs and results outside sim. Variables have defaults (reset_test, seed 1, UVM_LOW).

## Slide 11: Makefile: regression flow
1. Compile once
One VCS build in out/build_regression
2. Run 17 tests
Test chosen at run time, same seed
3. Check each log
UVM_ERROR and UVM_FATAL both 0
4. Write summary
PASS or FAIL per test in results/
5. make cov
urg merges coverage of all tests
vcs -sverilog -f build.flist -ntb_opts uvm-1.2 -timescale=1ns/1ps \
-cm line+cond+fsm+tgl+branch+assert -full64 -debug_access+all
./simv -cm_name $t +UVM_TESTNAME=$t +ntb_random_seed=$(SEED)
Out, logs and results folders are created automatically. Every simulation log is parsed by scripts/parse_log.py.
AXI2APB Bridge · UVM Verification
11
Notes: Key design choice: the UVM test name is a run-time plusarg, so the regression compiles only once instead of 17 times. Coverage metrics enabled: line, condition, FSM, toggle, branch and assertion.

## Slide 12: Regression and coverage results
17/17
tests pass
0
UVM errors, 234+ transactions checked
100%
functional coverage
Functional
100.00%
Line
~80.00%
FSM
60.00%
Condition
45.45%
AXI2APB Bridge · UVM Verification
12
Notes: Final regression: all 17 tests finished with UVM_ERROR 0 and UVM_FATAL 0. Functional coverage reached 100 percent with the coverage closure test. Structural coverage is lower; the next slide explains why.

## Slide 13: Why structural coverage is below 100%
FSM 60%
IDLE to SEND_B_RESP and IDLE to DONE_SINGLE_RD need a true zero-wait APB reply.
A blocking-assignment driver raised FSM to 80% but caused delta-cycle races and read mismatches. It was reverted to a stable clocked driver.
Condition 45.45%
The RTL has dead, parameterized code.
fifo.sv tests DEPTH == 0 but DEPTH is fixed at 4, and PSEL is hard-wired to 1, so these conditions cannot toggle.
Line ~80%
Uncovered lines are unreachable.
They sit in the FSM default case and in unused FIFO branches.
Decision: testbench stability was preferred over inflating FSM coverage. All gaps are documented as testbench limitations or RTL structure, not DUT bugs.
AXI2APB Bridge · UVM Verification
13
Notes: This is the engineering trade-off from the report. The FSM transitions that need a combinational zero-wait response are a testbench limitation. No DUT bug was found.

## Slide 14: Conclusion
All 17 tests pass with zero UVM errors and zero scoreboard mismatches
ID and USER propagation, wait states and back-pressure are verified
Functional coverage is 100%; structural gaps are analysed and documented
Documented RTL behaviour: single-beat only, WSTRB and PSLVERR ignored
Sign-off status: complete
Reproduce
cd sim
make allclean
make regression
make cov
GitHub repository
github.com/Muhammad-sheharyar/AXI-2-APB_Bridge_UVM_Verification
Muhammad Sheharyar · Submitted to Engr. Shahbaz Ahmad
14
Notes: Close with the sign-off and the reproduce steps. The repository link is in the box on the right. Thank the instructor and take questions.